## Slide 1
SortSense
AI-Based Waste Identification & Segregation
“Every item in the right bin — decided in under a second, at the point of disposal.”
Team Name: team_name
Team Members: Arpit Seth • Rajeev Maheshwari • Garv Agarwal
Sociothon 2026 • NSS IIT Roorkee • Smart & Sustainable Waste Management

## Slide 2
THE PROBLEM
What challenge are we solving?
1
Mixed at source
Wet, dry and hazardous waste end up in one bin — so recyclables get contaminated and become unrecoverable.
2
People don’t know
“Is a chip packet recyclable? A paper cup?” Confusion at the bin is the #1 cause of wrong disposal.
3
No data, no feedback
Nobody measures segregation quality per hostel or canteen, so nothing improves over time.
Result: recyclable value is lost to landfill, sorting staff hand-pick through mixed waste, and campuses can’t prove progress.

## Slide 3
THE IDEA
SortSense — a smart segregation station + app
Point a camera at any item. SortSense identifies it, tells you (and the bin) which compartment it goes in, and logs the decision — turning every disposal into clean segregation and live data.
Who it’s for
Students & staff at the bin • Housekeeping / sorting teams • Estate office & NSS volunteers
Biodegradable
Food, peels, tea leaves, leaves
Recyclable
PET bottles, cans, paper, cardboard
Non-recyclable
Multi-layer wrappers, tissues, thermocol
Hazardous / E-waste
Batteries, bulbs, sanitary, chargers

## Slide 4
HOW IT WORKS
From item to correct bin in under a second
1
Capture
Camera at the bin (ESP32-CAM) or phone app snaps the item
2
Classify
On-device MobileNet / YOLO model predicts the material
3
Decide
Confidence ≥ 80% → auto-route. Lower → ask the user
4
Route
LED + voice guide; servo flap opens the right lid
5
Learn
Every decision logged → dashboard + retraining
Handling errors: low-confidence items never get auto-dumped — the user confirms, and that confirmation becomes a new labelled training image.

## Slide 5
KEY FEATURES
1
Instant AI classification
4-category output with disposal instructions specific to the item
2
Confidence-aware routing
Uncertain predictions trigger a 1-tap human confirm, not a guess
3
Contamination alert
Flags wet waste or food residue going into the recyclable bin
4
Works offline
TFLite model runs on the device — no internet needed at the bin
5
Segregation dashboard
Per-hostel accuracy, volumes and trends for the estate office
6
Nudges & leaderboard
Hostel-vs-hostel segregation scores drive behaviour change

## Slide 6
INNOVATION
“What makes it different?”
THE DIFFERENTIATOR
Typical smart bin
Black-box classifier, guesses on every item
Needs cloud + Wi-Fi at each bin
₹20k–1L+ per unit, replaces bins
No data on who segregates well
SortSense
Knows when it doesn’t know → asks a human
Runs on-device, offline
≈ ₹4k retrofit kit on existing 3-bin sets
Every disposal feeds a live dashboard + retraining

## Slide 7
TECH STACK
AI / ML
MobileNetV2 transfer learning (TensorFlow/Keras) → TFLite & TF.js; YOLOv8n for multi-item detection
Datasets
TrashNet, TACO + our own campus images collected via the app’s confirm flow
Hardware
ESP32-CAM, SG90 servo flap, HC-SR04 fill sensor, RGB LED, buzzer
App / Web
HTML + JavaScript (TF.js) prototype; React Native / PWA for students
Backend
FastAPI + SQLite/PostgreSQL; MQTT from bins; Chart.js dashboard

## Slide 8
IMPACT & SCALABILITY
~75 t
recyclables recovered per year on one campus*
≥85%
target classification accuracy (TrashNet benchmark)
<1 s
on-device decision time at the bin
Scale path
1 hostel pilot
All hostels + canteens
Partner campuses
Municipal wards / RWAs
*Estimate: 8,000 residents × 0.3 kg/day, 25% recyclable share, clean-recovery rising from 40% to 75%. To be validated in the pilot.

## Slide 9
IMPLEMENTATION & COST
Item | Unit cost (₹)
ESP32-CAM module | 700
Servo flap + mount | 600
Fill sensors (×3) + LED + buzzer | 450
Power supply & wiring | 650
Enclosure / retrofit on existing bins | 1,600
Per station (approx.) | ≈ 4,000
Rollout
Wk 1–2: pilot 10 stations in one hostel
Wk 3–6: fine-tune on campus images
Month 2–3: all hostels + canteens
Pilot budget ≈ ₹55,000 incl. 2 gateways
Risks: lighting & dirty items (→ fallback confirm), vandalism (→ sealed enclosure), user fatigue (→ leaderboard nudges)

## Slide 10
FROM IDEA TO IMPACT
“Segregation fails at the first second — so SortSense makes that second smart, cheap, and measurable.”
ONE POWERFUL STATEMENT